## Slide 1: TELESCOPE CONTROL SOFTWARE
© C2PU, Observatoire de la Cote d’Azur,
Université de Nice Sophia-Antipolis
Jean-Pierre Rivet
CNRS, OCA,
Dept. Lagrange
jean-pierre.rivet@oca.eu
Version 04, 15/08/2017
Notes: Conférence présentée à PARSEC, le 1er octobre 2005.

## Slide 2: Launching the TCS
On the Telescope control computer’s desktop,
double left-click on the TCS software icon:
TCS: Telescope Control System (or Software)
Unless otherwise specified, always use the icon with
the highest version number (here: 76).

## Slide 3: Launching the TCS
A banner pops up, asking for permission
to switch the power boards on:
TCS: Telescope Control System (or Software)
Answer “Yes” for a normal observation run,
or “No” for a debugging session.

## Slide 4: The TCS GUI
GUI: Graphic User Interface

## Slide 5: The TCS GUI
GUI: Graphic User Interface
Date / Time
Dome control
Tracking
modes
Prime focus
filters
Telescope’s
coordinates
Focalization
Meteo
conditions
Target infos
Telescope’s
keypad
Slit control
Hardware
control
Threads infos
Service zone

## Slide 6: The date / time zone
UTC Julian date
Date (Local Time)
Time (Local Time)
UTC time
True Local Sidereal Time

## Slide 7: The keypad zone
Hour angle  slow
Declination  fast
Declination < 0
Declination  slow
Hour angle  fast
Hour angle  slow
Declination  fast
Hour angle > 0
Declination > 0
Declination  slow
Hour angle  fast
Hour angle < 0

## Slide 8: The telescope’s coordinates zone
Right ascension (hh:mm:ss.s)
Declination (+dd°mm’ss.s’’)
Azimuth (ddd°mm’ss’’)
Airmass
Hour angle (hh:mm:ss.s)
Elevation (dd°mm’ss’’)

## Slide 9: The slit control zone
Start the dome’s
slit opening process
Start the dome’s
slit closing process
Stop any ongoing process

## Slide 10: The dome control zone
Start automatic
mode
Synchronize
dome’s encoder
(requires privilege)
Dome rotation
Stop
Dome rotation
West
Set dome in
park position
Corrected
target
azimuth (*)
Dome rotation
East
Validate azimuth
correction (*)
Dome’s
azimuth (*)
(*) more on that later...

## Slide 11: Azimuth correction
Main
instrument
Auxiliary
instrument
Optical axes
offset
Far from meridian, the dome azimuth
must be corrected for the optical axis offset

## Slide 12: The focus zone
Focus 
Focus 
Focus index

## Slide 13: The prime focus filter zone
The F/3.2 coma-corrected prime focus of the Omicron@C2PU telescope
has a built-in 6-slots computer-controlled filter loader:
No filter
Filter 1
Filter 2
Filter 3
Filter 4
Filter 5
Filter 6
NOTA: the 6 filters have to be chosen once for all at the beginning of the training period, among the following list of available filters:
SDSS (Sloan) g’, r’, i’ or z’
Astro-photographic (Baader) R, G, B, or Luminance
H (BW=5nm)
O-III (BW=8.5nm)

## Slide 14: The tracking mode zone
Telescope
is halted
Telescope is
locked on its
target
Tracking type
Hour angle
offset (’’)
Declination
offset (’’)

## Slide 15: The target zone
Name
Right Ascension
Declination
Hour angle
Equatorial cords.
or object name
Select from a
scroll list
Solar System
planets
Asteroids,
comets
Azimutal cords.
Azimuth
Elevation
Airmass
Visual magnitude
Target’s apparent
EOD coordinates
Target’s defined by:
Synchronize
encoders
Set telescope
in park position
Slew to
target
Satellites

## Slide 16: Enter azimuthal coordinates
Define the target by its azimuth and elevation
NOTA: input formats:
type 180 for 180° 00’ 00’’
type 145 12 for 145° 12’ 00’’
type 110 21 34 for 110° 21’ 34’
type 91.5 for 91° 30’ 00’’
... then left-click on OK to validate, or on Cancel to dismiss
Enter azimuth
Enter elevation

## Slide 17: Enter equatorial coordinates
Method 1: Define the target by its name
Enter target’s identifier
(ex: M31, Aldebaran,
HD209458, NGC7635,
4UCAC556-032452 ...)
Then left-click on the button
“Find objects coordinates”
The software launches
automatically a request to
a WEB stellar database
(SIMBAD database at CDS).

## Slide 18: Enter equatorial coordinates
Method 1: Define the target by its name
... then left-click on OK to validate, or on Cancel to dismiss
The target’s name and
equatorial coordinates
should appear within seconds.

## Slide 19: Enter equatorial coordinates
Method 1: Define the target by its name
Should an error message pop up, then:
check internet connectivity
check spelling and syntax of the object’s identifier
(connect to http://simbad.u-strasbg.fr/simbad/sim-fid
and try to enter the identifier)
contact a local staff member and try Method 2.

## Slide 20: Enter equatorial coordinates
Method 2: Define the target by its equatorial coordinates
Enter target’s name
... then left click on OK to validate, or on Cancel to dismiss
Enter target’s
equatorial coordinates
Select the type
of coordinates

## Slide 21: Enter equatorial coordinates
Method 2: Define the target by its equatorial coordinates
PERMITTED FORMATS:
for right ascension (default unit: hours)
12 32 23 for 12h 32m 23s
12 32 for 12h 32m 00s
12 for 12h 00m 00s
14.50 for 14h 30m 00s
30.5 d for 30.5 degrees (02h 30m 00s)
for declination (default units: degrees)
20 54 36 for +20° 54’ 36’’
+20 54 36 for +20° 54’ 36’’
20 54 for +20° 54’ 00’’
20 for +20° 00’ 00’’
20.5 for +20° 30’ 00’’
20.5d for +20° 30’ 00’’

## Slide 22: Choose from a list of targets
... then left-click on OK to validate, or on Cancel to dismiss
Displays a list of “popular” targets
Left-click on the desired line

## Slide 23: Solar System major objects
... then left-click on OK to validate, or on Cancel to dismiss
Displays a list of Solar System planets
Left-click on the desired object

## Slide 24: Solar System minor objects
... then left-click on OK to validate, or on Cancel to dismiss
Define the target (asteroid, comet) by its identifier
Enter object’s name
(ex: Toutatis, 868, 2012DA14...)
Then left-click on the button
“Find objects coordinates”
Select the type of object
The software launches
a request to a WEB ephemeris
server (IMCCE).

## Slide 25: Solar System minor objects
Define the target (asteroid, comet) by its identifier
Should an error message pop up, then:
check internet connectivity
check spelling and syntax of the object’s identifier
contact a local staff member.

## Slide 26: Solar System minor objects
... then left-click on OK to validate, or on Cancel to dismiss
Define the target (asteroid, comet) by its identifier
Select the type of tracking:
Sidereal: telescope locks on the
initial position of the (moving) object
Differential: telescope locks on the
object itself (proper motion taken
into account)
Half-speed: telescope follows the
object, but with half is proper motion speed.
The target’s name and
equatorial coordinates
should appear within seconds.

## Slide 27: Earth’s artificial satellites
TLE file browser
Editor for
NORAD’s TLE
(Two Lines Elements)
Satellite selector
Tracking mode
selector
Clear all
Validate the choices
Exit without validation

## Slide 28: Option 1: cut-and-paste TLEs
Cut-and-paste
TLEs here

## Slide 29: Option 1: cut-and-paste TLEs
Left-click here
to update the
satellite list

## Slide 30: Option 1: cut-and-paste TLEs
Left-click on the
wanted satellite
to select it

## Slide 31: Option 1: cut-and-paste TLEs
Choose the
tracking mode ...
... then left-click
here to validate,
... or here
to dismiss.

## Slide 32: Option 2: get TLEs from a file
Left-click here to
open the file browser

## Slide 33: Option 2: get TLEs from a file
Navigate and select
the wanted TLE file

## Slide 34: Option 2: get TLEs from a file
Select the
satellite ...
Choose the
tracking mode ...
... then left-click
here to validate,
... or here
to dismiss.

## Slide 35: Check target’s observability
The target’s name and
apparent, refracted EOD
equatorial coordinates
are displayed in the
target zone
CHECK that the target is
in the observable zone !

## Slide 36: Observable zone
Elevation:
h > 18°
Declination:
< 60°
Hour angle:
-6h < H < +6h

## Slide 37: Go to target !
Left-click on the
“Go to target”
button
A confirmation banner pops up ...
... then left-click on OK to validate, or on Cancel to dismiss

## Slide 38: Interrupt the telescope’s slew
The “Go to target” thread
indicator turns green
If you need to interrupt
the telescope’s slew process,
left-click on the
“Go to target” thread indicator, which
should turn red within seconds:

## Slide 39: Start the automatic dome control
The azimuth correction requires some geometrical
parameters (auxiliary instrument optical axis offset).
They should be entered in a configuration file
by an authorized staff member only.
TO BE DONE ONLY IF AN AUXILLIARY
OFF-AXIS OPTICAL INSTRUMENT IS USED !!!!
Left-click here to
validate the
azimuth correction
for shifted optics
The corrected
azimuth
appears here

## Slide 40: Start the automatic dome control
The dome’s slit should slew automatically and stop
in front of the instrument’s aperture.
The dome’s position is corrected automatically
when needed.
Left-click on the
“Auto” button

## Slide 41: Manual dome control
If needed,
left-click on the
“Auto” button
to come back
to manual mode
Left-click on these
buttons to
move the dome
NEVER use
this button !
(authorized staff only)

## Slide 42: To end the observations
Left-click on the
“Mount park” button
STEP 1: park the mount
A confirmation banner pops up ...
... then left-click on OK to validate, or on Cancel to dismiss

## Slide 43: To end the observations
... then
left-click on the
“Park” button
If needed,
left-click on the
“Auto” button
to come back
to manual mode ...
STEP 2: park the dome

## Slide 44: To end the observations
... then wait until the
“STOP” button becomes
disabled (grayed)
Left-click on the
“Close” button...
STEP 3: close the dome

## Slide 45: To end the observations
Left-click on the
“EXIT” button
The TCS shutdown process last some 20 seconds.
When the GUI disappears, the shutdown process is completed.
STEP 4: shutdown the TCS software

## Slide 46: To end the observations
If a confirmation pop-up window appears:
... left-click on “OK”

## Slide 47: END

## Slide 48
END